1. Write the transformation matrix that rotates around the origin by a counterclockwise angle of θ = π/6 radians. If I applied this to the point (10, 20), what are the (x, y) coordinates of the resulting point?

R(π/6) =
| cos(π/6) -sin(π/6) |
| sin(π/6) cos(π/6) |

P	= | 10 20 |T

P'	= P * R
P'	= 10*cos(π/6) + 20*-sin(π/6) , 10*sin(π/6) + 20*cos(π/6)
= (9.816814532, 20.090548834)

2. Write the transformation matrix that translates by an offset of (30, −50). If I applied this to the point (10, 20), what are the (x, y) coordinates of the resulting point?

T(30, -50) =
| 30 |
| -50 |

P	= | 10 20 |T

P'	= P + T
= 10 + 30 , 20 + -50
= (40, -30)

3. Write the transformation matrix that scales uniformly by a factor of 3. If I applied this to the point (10, 20), what are the (x, y) coordinates of the resulting point?

S(3) =
| 3 0 |
| 0 3 |

P	= | 10 20 |T
P'	= P * S
= 10*3 + 20*0 , 10*0 + 20*3
= (30, 60)

4. Write the transformation matrix that scales nonuniformly by a factor of 2 horizontally and 5 vertically. If I applied this to the point (10, 20), what are the (x, y) coordinates of the resulting point?

S(2, 5) =
| 2 0 |
| 0 5 |

P	= | 10 20 |T
P'	= 10*2 + 20*0 , 10*0 + 20*5
P'	= (20, 100)

5. Write the transformation matrix that will apply a shearing transform where x = x and y = 3x + y. If I applied this to the point (10, 20), what are the (x, y) coordinates of the resulting point?

Sh(x, 3x+y) =
| 1 0 |	=	| x |
| 3 1 |	| 3x+y |

P	= | 10 20 |T
P'	= P * Sh
= 10*1 + 20*0 , 10*3 + 20*1
= (10, 50)

6. Rotation around an arbitrary center of rotation c can be done by applying a translation by an offset of −c, rotating by the desired angle, and then translating by an offset of +c. Write an equation that would give you a single linear transformation rotates counterclockwise by an angle of θ = π/4 radians around the point 40, 50. You do not have to actually calculate this matrix—write it as the product of multiple other matrices. If I applied this sequence to the point (45, 50), what are the (x, y) coordinates of the resulting point?

T(40, 50) =
| 40 |
| 50 |

R(π/4) =
| cos(π/4) -sin(π/4) |
| sin(π/4) cos(π/4) |

P'	= ((P-T)*R)+T

P	= | 45 50 |T

P'	= ([5, 0]T*R)+T
= ([5*sqrt(2)/2, 5*sqrt(2)/2]T)+T
= | 5/2*sqrt(2)+40 5/2*sqrt(2)+50 |T

7. A square of length 20 on each side is centered at (100, 80) in world coordinates and tilted counterclockwise by an angle of π/4 radians. Write an equation that would give you a single transformation matrix that maps points in object coordinates to world coordinates. Where is the upper right corner of the square ((10, 10) in object space) in world coordinates?

T(100, 80) =
| 100 |
| 80 |

R(π/4) =
| cos(π/4) -sin(π/4) |
| sin(π/4) cos(π/4) |

Pw	= (P*R)+T

P	= | 10 10 |T

PW	= ([10, 10]T*R)+T
= ([10*(cos(π/4) + -sin(π/4)), 10*(sin(π/4) + cos(π/4))]T)+T
= ([10*0, 10*sqrt(2)]T)+T
= | 100 10*sqrt(2)+80 |T

8. Using the same square as in Question 7, write an equation that gives you a single transformation matrix that maps points in world coordinates to object coordinates. Use this to determine whether the point (90, 90) is in the square.

PO	= (P+T)*R

Po	=
| cos(π/4) sin(π/4) -100 |
| -sin(π/4) cos(π/4) -80 |
| 0 0 1 |

P	= | 90 90 1 |T

PO	= | 90*cos(π/4)+90*sin(π/4)+1*-100 90*